## Slide 1: - L359 - Sill / Lower A post ticking noise elimination

## Slide 2: Viewing Area and Explanation
The RH front jacking point is the focus of the ticking noise investigation and elimination.
All following pictures viewing the inner sill are taken of the buck. In normal built up vehicles the sill is in a closed box condition.
Notes: Remove sill cladding and rear grommet

## Slide 3
Sill / Lower A post ticking noise elimination
The reinforcing panel (see black arrow in picture) can touch the outer sill at the top rear corner (yellow arrow) during body movements causing a ticking noise.
In the further slides the elimination of this unwanted and disturbing noise, which is audible inside the cabin under normal driving conditions, is explained.
Outer sill

## Slide 4: Sill / Lower A post ticking noise elimination
Insert a screwdriver into sill in the hole next to jacking point.
Ensure that the screwdriver is Parallel to jacking point and insert to approx 120mm. You will feel some resistance at approx 90mm when it contacts the panel, it will now need knocking firmly upwards to push up between the reinforcing panel and outer sill. When it hits a hard stop (120mm), give the screwdriver a few more firm knocks to separate the panels.

## Slide 5: Sill / Lower A post ticking noise elimination
The screwdriver must be on this side of the baffle which would measure approx 120mm (see picture).
Now the reinforcing panel can be distorted away from the outer sill to eliminate the unwanted noise.

## Slide 6
This is the wrong condition do not approach panel from the sill side hole, the insertion length will only be approx 110mm and there will be no 90mm resistance.
Sill / Lower A post ticking noise elimination
Doing this would have no effect on the ticking noise!